Gagasan & Inovasi / Ulasan (delete yang tidak perlu)

# Emerging Trends in Economic Development and River Water Quality in Banten Province, Indonesia: One Decade after Decentralization Policy Implementation (2000-2010)

*Endan Suwandana1, Kensuke Kawamura2 and Dessy Arianti3

1 Marine  and Fisheries Office of Banten Province, Jl. Syeh Nawawi Al-Bantani (KP3B), Palima - Curug, Serang 42171, Banten Province, Indonesia

2 Graduate School for International Development and Cooperation, Hiroshima University, 1-5-1 Kagamiyama, Higashi-Hiroshima 739-8529, Japan

3 Water Resources Office of Banten Province, Jl. Syeh Nawawi Al-Bantani (KP3B), Palima, Serang 42171, Indonesia

(Diterima 5 Januari 2014; Direvisi 12 Pebruari 2014; Disetujui 20 Pebruari 2014; Diterbitkan 11 Maret 2014)

Abstract: This study analyzes the economic growth of Banten Province and river water quality (as environmental indicator) one decade after decentralization. Descriptive and multivariate statistics were used in data analysis. The results showed that Banten Province has achieved well economic growth. Its GDP has contributed to approximately 14.75% of the national GDP. At the same time, the population growth has increased significantly with an annual rate of 2.78. Nine physicochemical elements in Ciujung River showed increasing trends, especially in the last five years. Some parameters even exceeded their ambient values. Among the heavy metals, seven elements exhibited intensifying concentrations. Out of seven, iron has exceeded its ambient level. The organic materials in Ciujung River were also very high, indicated by the level of KMnO4 and Escherichia coli concentration. The multivariate statistics revealed that, although some elements showed intensifying concentrations, seasonal variability still played an important role in the water changes.

Keywords: autonomy policy, sustainable development, river pollution, multivariate.

▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬

Corresponding author: Endan Suwandana, E-mail: endan2006@yahoo.com, Tel. +62-254-267024.

## Pendahuluan

The decentralization (autonomy) policy has been implemented in Indonesia since 1999 (Seymour and Turner, 2002). Since then, eight new provinces have been established, including Banten Province, to add up a total number of 33 provinces. By this policy, each province has its own freedom to self-govern and manage their budget and development planning with less interference from the central government (Yonariza and Shivakoti, 2008). By 2011, this policy has resulted in the creation of new economic regions (Firman, 2011).

For some countries, economic development is like a coin. It has two side effects; one side can create regional development that leads to human prosperity, and the other side can create environmental quality degradation and land cover change (Abdullah and Nakagoshi, 2006; Hasse and Lathrop 2003; Stagl, 1999). The negative effects of regional development can actually be minimized by good management (Collin and Melloul, 2003; Chakrabarty, 2001), but in most cases especially in developing countries, this is what usually too complex to be implemented (Rakodi, 2001). Jakarta city and Ciliwung watershed is an example wherein economic development and environmental degradation, i.e., air and water pollution, show strong negative correlation (Suwandana et al., 2011; Colbran, 2009; Steinberg, 2007).

Figure 1. Trends of human population, electricity customers, electricity consumption in Banten Province during the period of 2001 – 2010

Xxxxxxxxxx

Xxxxxxxxxx

Xxxxxxxxxx

## Analisa

In the last ten years, the human population in Banten Province has increased from 8 million to 10.6 million with a provincial birth rate of 2.78 (Figure 2). The population growth has an implication on the increase of the electricity customers for almost 500% from 444,924 to more than 1.9 million customers. Consequently, the need of electricity consumption has also increased from 4.27 billion Kwh to 16.3 billion Kwh, in which a significant leap occurred in 2008. Besides household consumption, the number of new established factories has given much contribution to the need of electricity.

In agriculture sector, Figure 3 illustrates the production increase in some important commodities, such as rice, chickens and ducks. For the last decade, the production increase has reached an average of 0.18 million ton•year-1, 2.82 million ton•year-1, 0.71 million ton•year-1, 0.35 million ton•year-1 and 0.11 million ton•year-1, corresponding to paddy, chicken broilers, chicken broilers (native species), chicken egg layers, and ducks.

Table 1. Minimum, maximum, mean and standard deviation of water quality parameters of Ciujung River compiled from 9 stations during 2000 – 2010.

| Parameter | Unit | Min | Max | Mean | Standard deviation | Coefficient of variance |
| --- | --- | --- | --- | --- | --- | --- |
| Temperature | ºC | 21.600 | 34.800 | 28.455 | 1.551 | 5.451 |
| DO | mg/l | 0.421 | 7.449 | 4.101 | 1.031 | 25.140 |
| COD | mg/l | 0.909 | 646.800 | 37.082 | 35.511 | 95.763 |
| BOD | mg/l | 0.168 | 30.210 | 2.426 | 3.509 | 144.641 |
| Chromium | mg/l | 0.000 | 0.029 | 0.008 | 0.008 | 100.000 |
| Lead | mg/l | 0.000 | 0.081 | 0.007 | 0.007 | 100.000 |
| Zinc | mg/l | 0.002 | 0.968 | 0.038 | 0.146 | 384.211 |

## Kesimpulan

The analysis was done for the water quality data at Jongjing station (the lower most station in downstream area of Ciujung River, into which the water from the upper regions accumulates). The results showed that the majority of the parameters were still below their threshold values. However nine physicochemical elements, seven heavy metal elements and two organic-material-related properties have shown the increasing trends during 10 years observation.

For nonmetal elements, there were eight parameters out of 41 water parameters at Jongjing station already beyond their ambient values. Those include turbidity, TSS, COD, salinity, nitrite, phenol, KMnO4 and E. coli. The concentration increase seemed to be related with the inputs from natural and domestic loads. Overall, this study revealed that Ciujung River is still considered to be relatively clean, but an emerging increase in heavy metals concentration could be taken as a serious warning for the local government.

Xxxxxxxxxx

Xxxxxxxxxx

Xxxxxxxxxx

## Ucapan terimakasih

The authors sincerely thank the Water Resources Office of Banten Province for the help in providing us with the water quality database. We would also acknowledge the financial support from the Global Environmental Leader (GEL) Project of the International Development and Cooperation (IDEC), Hiroshima University, and the National Development Planning Agency of Indonesia (BAPPENAS).

## Daftar Pustaka

Abdullah, S.A., & Nakagoshi, N. (2006). Changes in landscape spatial pattern in the highly developing state of Selangor, Peninsular Malaysia. Landscape Urban Planning, 77(3), 263-275.

Aldrian E., & Susanto, D. (2003). Identification of three dominant rainfall regions within Indonesia and their relationship to sea surface temperature. International Journal of Climatology, 23, 1435-1452.

Bilotta G.S., & Brazier, R.E. (2008). Understanding the inﬂuence of suspended solids on water quality and aquatic biota. Water Resources, 42, 2849-2861.

Buhl-Nielsen E., Giltner, S., Dutton, P., Donohoe, J., O’Farrell, S.E., & Setiawan, D. (2009). Independent evaluation of Australian aid to water supply and sanitation service delivery in East Timor and Indonesia. Retrieved from http://www.ode.ausaid.gov.au/

Chakrabarty, B.K. (2001). Urban management: Concepts, principles, techniques and education. Cities, 18(5), 331-345.

Colbran, N. (2009). Will Jakarta be the next Atlantis? Excessive groundwater use resulting from a failing piped water network. Law, Environment and Development, 5(1), 20-37.

Xxxxxxxxxxxxx

Xxxxxxxxxxxxx

Xxxxxxxxxxxxx

Abstrak: Studi ini menganalisa pertumbuhan ekonomi Provinsi Banten dan kualitas air sungai (sebagai indicator lingkungan) satu decade setelah otonomi daerah. Statistik deskpritif dan statistik multivariat digunakan di dalam analisa data. Hasil studi ini menunjukkan bahwa Provinsi Banten telah mengalami pertumbuhan ekonomi yang sangat baik. Nilai GDP Banten berkontribusi sekitar 14,75% pada nilai GDP secara nasional. Pada saat yang sama, Pertumbuhan penduduk juga telah meningkat secara signifikan dengan pertumbuhun rata-rata sebesar 2,78. Sembilan element fisika dan kimia dari kualitas air Sungai Ciujung menunjung tren meningkat, khususnya pada lima tahun terakhir. Beberapa parameter bahkan telah melebihi nilai ambang batasnya. Di antara logam berat, tujuh elemen telah menunjukkan konsentrasi yang meningkat. Dari elemen yang tujuh ini, iron telah melebihi nilai ambang batasnya. Material-material organic di Sungai Ciujung juga sangat tinggi, yang diindikasikan oleh level KMnO4 dan konsentrasi Escherichia coli. Statistik multivariat menjelaskan bahwa, walaupun beberapa elemen telah menunjukkan peningkatan konsentrasi, namun variabilitas musiman masih memainkan peranan penting dalam turut mempengaruhi perubahan kualitas air Sungai Ciujung.

Kata kunci: Kebijakan otonomi daerah, pembangunan yang berkelanjutan, polusi sungai, statistic multivariat.

▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬▬